## Slide 1: Prescription Drug Abuse And The Toxicology Of Medication Monitoring
Andrea Terrell, PhD, DABCC
Chief Scientific Officer
AIT Laboratories
Indianapolis, IN

## Slide 2: Prescription Drug Abuse
>125 million ED visits in 2011, 2.5 million (2.0%) drug misuse or abuse related
  27% illicit drugs only
  34% pharmaceuticals only
  35% combination (illicit, alcohol, pharmaceuticals)
2004 to 2011: 148% increase in ED visits related to pharmaceutical drug misuse or abuse (336K to 835K)
  Benzodiazepines up 149%
  Opioids up 183% (172K to 488K)
    All drugs except Propoxyphene saw an increase
Short term rates are slowing, still increasing
Data from DAWN reports

## Slide 3: Magnitude of Non-compliance

## Slide 4: Sample Opioid agreement (WA State)

## Slide 5: Overview of the testing process
Accession and order testing
Screen by Immunoassay or Mass Spectrometer
Confirm by Mass Spectrometer
  Confirm all positives
  Confirm prescribed meds, regardless of screen results
Certify results
Send lab report, ancillary information about results
Toxicologist interpretation

## Slide 6: Lack of Standardization
What is not standardized
  Panel components
  Screen method
  Confirmation method
  Cutoffs for screen
  Cutoffs for confirmation
  Who and when to test
  Venue for testing (in office or in laboratory)
What is standardized
  Accreditation of clinical labs

## Slide 7: Pain management panel components
Opioids
  6-MAM (metabolite of heroin, not always included)
  Hydrocodone
  Hydromorphone
  Morphine
  Codeine
  Oxycodone
  Oxymorphone
  Methadone
  Fentanyl
  Buprenorphine
Benzodiazepines
  Alprazolam metabolite
  Clonazepam metabolite
  Lorazepam
  Diazepam metabolite
  Oxazepam
  Temazepam
Alcohol
Drugs of abuse (cannabinoids, cocaine, methamphetamine)
Other therapeutics (Amphetamine, Barbiturates, Soma, Tramadol)
Specimen validity tests (pH, creatinine, adulterants)

## Slide 8: Heroin in pain management
Heroin metabolizes into 6-MAM and Morphine
  Codeine usually present as well
Not all Opiates analytical methods measure 6-MAM
SAMHSA process is to run 6-MAM if Morphine is detected
  Separate method
Of 152,000 pain management samples received, approximately 1300 (0.9%) were positive for 6-MAM
MORPHINE
HEROIN
6-MAM

## Slide 9: Analytical Methodology
Screen
  Immunoassay
    Lateral flow device – dipstick, cup
    Automated analyzer
  Mass spectrometry
Confirmation
  Mass spectrometry – provides 100% unequivocal identification
  Liquid or gas chromatography paired to the mass spec
  Immunoassay is not an acceptable confirmatory method
    Even if sold as “quantitative” or “semi-quantitative”
    Cannot detect the presence of a specific drug

## Slide 10: Cutoffs
Screen
  Manufacturer set cutoffs
    Opiates – 300 or 2000ng/mL
    Benzodiazepines – 200 or 300ng/mL
  Can validate to lower cutoffs
    Opiates – 50ng/mL
    Benzos – 75ng/mL
Confirmations
  Completely lab dependent

## Slide 11: Who and When to test
Risk based approach
Assess
Comprehensive testing
Characterize
Risk assessment
Monitor
Low: directed analyses for drugs prescribed
Low
High
Moderate
Moderate: limited panels
High: comprehensive testing, every time

## Slide 12: Instant and “screen only” testing
Reimbursement driving more physicians to implement some POC drug screening
Generally a cup, dipstick or automated analyzer used at the point of care/collection
Potentially valuable “truth serum”
Limitations exist:
  1. Sensitivity – cutoffs too high to detect the drug of interest
  2. Selectivity – not definitive, can’t distinguish between the drug of interest and other compounds in the sample

## Slide 13: True or False Positive?
Phentermine
Methamphetamine
Both give a positive on the amphetamine immunoassay screen

## Slide 14: Blood Testing
Typical specimen in compliance monitoring is urine
Blood analysis provides complementary, and unique information
Blood and urine cannot be compared directly as they provide different information:
  Urine is a more suitable matrix for identifying illicit, or non-prescribed drug use, has longer window of detection
  Blood is a more suitable matrix for evaluating the prescribed drug (eg. blood concentration relative to dose)
  Blood testing of pain management patients can play a crucial role in accident and death investigations

## Slide 15: Blood Study of Functional Pts. (Tennant et al, Practical Pain Management, March 2006)
Age/Sex | Drug | Blood Conc. | Normal | Toxic
42/F | Fentanyl Transdermal | 8.2 ng/mL | 1 – 3 | > 3
55/F | Codeine | 480 ng/mL | 30 – 120 | > 1000
48/F | Hydrocodone | 396 ng/mL | 10 - 40 | > 100
44/F | Methadone | 2580 ng/mL | 50 - 1000 | > 200
56/F | Morphine | 828 ng/mL | 10 - 80 | > 200
53/F | Oxycodone | 458 ng/mL | 10 – 100 | > 200
Study patients on therapy for 1-50 years
Blood collected 1-2 hours after regular dose
Normal & toxic ranges often don’t apply in chronic opioid therapy
Blood concentrations overlap those seen in death investigations
Routine blood testing for pain medications could be useful in the event of patient death or DUI charge
Tolerance must be considered when interpreting blood concentrations of an opioid

## Slide 17: Oral Fluid/Saliva
Ease of collection
Non-invasive
Procedural and analytical hurdles
  Some drugs cause dry mouth
  Difficult to obtain consistent volume
    Creates problem when using “buffered” device and quantitation is desired
  Often multiple drugs present, so volume could be insufficient
    On average 2.5 confirmations per urine sample (AIT data)
Urine more appropriate for qualitative compliance monitoring
Blood more appropriate for dosage compliance
OF may be useful alternative, challenges remain

## Slide 18: Opiate Metabolism
MORPHINE
HYDROCODONE
HEROIN
6-MAM
CODEINE

## Slide 19: Opiate Metabolism (cont.)
HYDROCODONE
HYDROMORPHONE
OXYMORPHONE
MORPHINE
OXYCODONE

## Slide 20: Anomalies in Medication Monitoring
The presence of morphine when morphine is not prescribed (dietary)
The presence of codeine when prescribing morphine (pharmaceutical grade impurity)
The presence of hydrocodone when prescribing oxycodone (pharmaceutical grade impurity)
The presence of 6-MAM when prescribing morphine (pharmaceutical grade impurity)
The presence of Hydromorphone when prescribing morphine (minor metabolic pathway)
The presence of Hydrocodone when prescribing Codeine
(minor metabolic pathway)

## Slide 21
Pill scraping – another possible trick when screening alone is used

## Slide 22: Thank you!
Andrea Terrell, PhD
aterrell@aitlabs.com
toxicologist@aitlabs.com

## Slide 23: FAQs
Can immunoassay be confirmatory?
Is it cost prohibitive to require UDM for every patient on an opioid?
Can the labs handle the volume of increased testing?
What are the limitations of sensitivity for low-dose semi-synthetic opioids?
Do most labs routinely do their own screening (IA) before proceeding to a confirmatory test? Or can Confirmatory be directly ordered. Do you only run confirmatory tests on positive screening?
What is the cost of screening vs. confirmatory tests?
Do you have any data validating typical urine levels for different doses of opioids?
What are the different pain panels typically?
What is the turn-around time for confirmatory testing?
Is there any clinical utility to knowing the actual level of a drug in the urine?
Are there false positives with GC/MS testing ?
If this becomes law...can most physicians assume that a certified lab that advertises confirmatory testing is using low-thresholds? Is there a lab standard for thresholds for confirmatory testing? IS there a lab standard for thresholds for screening testing?
How much urine is needed?