Facility Name		                                                          		                        Biochemical Oxygen Demand       	    SM 5210 B.

IN	           OUT

Analysis Date:________________	Chlorine Present   Yes  /  No  					Analyst:		  ___________          ___________

Read Date:___________________	Chlorine removed by:___________________________________	Incubator Temp oC:	  ___________          ___________

___________________________________	Time:			  ___________          ___________

Dilution Water Prepared on____________________ 	Dilution Water pH___________ SU

(Complete this box unless separate calibration form used.) Analysis Date: Barometric Pressure/Temperature:________mm Hg/_______oC Meter/Probe Calibrated by:____________ Time:____________ Read Date: Barometric Pressure/Temperature:________mm Hg/_______oC Meter/Probe Calibrated by:____________ Time:____________

| Sample ID | Sample Date | Grab or Comp | Bottle ID | Sample mL | Seed Added mL | Inhibitor Added ? | Setup Temp. oC | Initial DO mg/L | Final DO mg/L | DO Depletion mg/L | Seed Correction mg/L | Correction Depletion mg/L | BOD5 (mg/L) | BOD5 Average mg/L |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Blank 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Blank 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Seed 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Seed 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| G/GA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| G/GA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Final 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Final 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Final 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Final Dup |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pri Eff 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Pri Eff 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Raw 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Raw 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Raw 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Raw Dup |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Calculations:  Calculate only those samples that have a Final DO greater than or equal to ( ≥ ) 1.0 mg/L and a DO Depletion greater than or equal to ( ≥ ) 2.0 mg/L

Unseeded BOD5 (mg/L) = DO Depletion x 300 mL			Seeded BOD5 (mg/L) = Seed Corrected Depletion x 300 mL

mL Sample                                                                                                          mL Sample

Seed Correction = [(Seed 1 DO Depletion/mL Seed Added)+(Seed 2 DO Depletion/mL Seed Added)] x mL Seed Added to Samples

2

Seed Corrected Depletion = DO Depletion – Seed Correction                                                                                                                                                  BOD5 Created 1/2009