## Slide 1: Intersection Improvement U.S. 24 at C.R. 300 East in Wabash County
Indiana Department of Transportation
Wednesday, March 20, 2019
6 p.m.

## Slide 2: Welcome
Purpose/explanation of public hearing
Public hearing format
Visit our sign-in table
Informational handouts
Participate during public comment session
Submit written public comments
Project display area

## Slide 3: U.S. 24 at C.R. 300 East Intersection Improvement
Introduction of INDOT Project Team
  Fort Wayne District – INDOT Regional Office
  Project Management
  Communications
  Environmental Services
  Public Involvement Team
  Strand Associates, Metric Environmental
    Engineering, Design & Environmental Analysis
Recognition of elected and local public officials
Sign-in at attendance table to be added to project mailing list
Legal notice of public hearing was published in the Wabash Plain Dealer 3/5/19 & 3/12/19
A notice of the public hearing was mailed to known property owners within project area
Announcement of this hearing was posted to INDOT website; media release issued
A copy of presentation and project documentation are available for review on-line via INDOT website https://www.in.gov/indot/3896.htm

## Slide 4: Project Stakeholders
Indiana Department of Transportation
Indiana Division Federal Highway Administration
Wabash County
Elected & local officials
Residents and citizens
Commuters
Businesses
Emergency services
Schools
Churches
Community Organizations

## Slide 5: Project Development
Project Selection
Early Coordination
Environmental phase begins
Purpose & Need
Develop alternatives
Preliminary design phase
Release environmental document for public review and comment
HOLD PUBLIC HEARING
Additional work to finalize environmental document and project design
Communicate Project Decision
Project Letting
Construction

## Slide 6: Environmental Analysis Phase
  National Environmental Policy Act (NEPA)
  Requires INDOT to analyze and evaluate the impacts of a proposed project to the natural and socio-economic environments
  NEPA is a decision-making process
    Purpose and Need
    Alternatives Screening
    Preferred Alternative
  Impacts are analyzed, evaluated and described in an environmental document
    What are the impacts this project might have on the community?
    How can impacts be avoided?
    Can impacts be minimized?
    Mitigation for impacts?
  Draft environmental document released for public involvement – February 2019
    Available for review at project resource locations

## Slide 7: Examples of Items Evaluated during Analysis
  Right-of-Way
  Streams, Wetlands, and Other Waters
  Floodplains
  Endangered Species
  Farmland
  Cultural Resources (Historic/Archaeological)
  Parks and Recreational Lands (Trails)
  Air Quality
  Noise
  Impact to residential and commercial properties
  Environmental Justice
  Hazardous Materials
  Permits
  Mitigation

## Slide 8: Project Resource Locations
INDOT Fort Wayne District Office
  5333 Hatfield Road, Fort Wayne, Indiana 46808
  Planning, Project Development/Delivery, Construction, Maintenance for Northeast Indiana
  http://www.in.gov/indot/2703.htm
Wabash Carnegie Public Library
188 West Hill Street, Wabash, IN 46992
Phone: (260) 563-2972
INDOT Office of Public Involvement
  100 North Senate Avenue, Room N642, Indianapolis, IN 46204
  Phone: (317) 232-6601
  rclark@indot.in.gov
Transportation Services Call Center
Provides citizen and business customers with a single point-of-contact to request transportation services, obtain information, or provide feedback through multiple channels of communications.
855-463-6848 • INDOT4U.com • INDOT@indot.in.gov

## Slide 9: Intersection Improvement – Purpose & Need
Purpose: Enhance safety at intersection
  Analysis indicates high number of vehicular collisions at intersection
  Severity of collisions due to type of accidents at this location
Need: Decrease number and severity of high-speed collisions at this location
  Right-angle collisions occurring at this location
    Resulting in higher severity and increased injury

## Slide 10: Intersection Data
Year | Fatal | Injury | Property Damage | Total
2014 | 0 | 2 | 1 | 3
2015 | 0 | 1 | 4 | 5
2016 | 0 | 0 | 1 | 1
2017 | 0 | 1 | 4 | 5
2018 | 0 | 0 | 1 | 1
Totals | 0 | 4 | 11 | 15
All crashes were right-angle
80% of crashes involved northbound and westbound vehicles
Most recent fatality in 2009
Identified as a high-crash location by frequency and severity
  Lagro Road: 560 vehicles per day
  US 24: 9,000 vehicles per day

## Slide 11: Previous Countermeasures
Overhead Flashing Beacons – Advanced Signage

## Slide 12: Alternatives Analysis
NOTE: Each alternative analyzed for 20 years after construction
No Build
  Involves regular maintenance activities
  Cost: $0
  Does not enhance safety; does not meet purpose and need of project
Traffic Signal
  Cost: $300,000-$500,000 (includes operating cost)
  Lagro Road does not meet signal warrants
  Signals on high-speed roadways:
    Are less efficient, causing vehicles traveling 60+ mph to slow down or stop
    Are susceptible to red-light running
    Can cause an increase in crashes where not warranted, per a Purdue University study
  No signals between SR 13 in Wabash and SR 9 in Huntington

## Slide 13: Alternatives Analysis
Median U-Turn
  Cost: $650,000-$900,000
  Enhances safety by prohibiting county road through traffic from crossing U.S. 24 at the intersection
  Meets purpose and need of project
High-Speed Roundabout
  Cost: $2-3.5 million
  Would require traffic on US 24 to slow to approx. 25 mph

## Slide 14: Alternatives Analysis
Grade Separation
  Cost: $3-5 million
  Affects intersection mobility
Interchange
  Cost: $12-15 million
  Does not fit scale of project because of low-volume road
  Requires significant time for planning and construction

## Slide 15: Preferred Alternative: Median U-Turn
Additional Pavement
Removed Pavement
US 24
Lagro Rd.

## Slide 16: Median U-Turn Operations
US 24
Lagro Rd.

## Slide 17: Median U-Turns Enhance Intersection Safety
Conflict points are dramatically reduced
Crossing points eliminated, reducing crash severity
Conventional
Intersection
Median U-Turn
Intersection

## Slide 18: Design Features
Wider median shoulder (8’) to accommodate farm equipment
Diagrammatic signs on each approach
Improving drainage issue on northbound approach
Delineators emphasize no through movement on Lagro Road
Raised Pavement Markers delineate U-Turn lanes

## Slide 19: Recap of Alternatives Considered
No Build
  No additional work; crashes continue
Signalized Intersection
  Traffic on minor leg (Lagro Road) does not warrant a signalized intersection when compared to traffic on major leg (US 24)
  Not best fit on high-speed roadway with no other signals
Roundabout
  Higher cost; slows traffic on US 24
Grade Separation: Lagro Road over US 24
  Limits mobility, significant increase in project cost
Interchange
  Implementation would require years of planning and design
  Highest project cost
Median U-Turn Intersection
  Enhances safety at intersection by eliminating or significantly reducing injury crashes
  Cost-effective
  Can be implemented in one construction season and be delivered next year

## Slide 20: Schedule and Maintenance of Traffic
Spring 2020
3 to 6 month duration
Maintenance of Traffic
  Closed intersection to provide highest contractor and driver safety as well as shortest construction duration
  Traffic to/from school could use SR 524 to US 24 to SR 13

## Slide 21: Submit Public Comments
Submit public comments using the options described in first page of information packet:
  Public Comment Form
  Via e-mail at rclark@indot.in.gov
  Participate during public comment session following formal presentation
INDOT respectfully requests comments be submitted by Friday, April 5, 2019
All comments submitted are included in public hearings transcript and made part of the public record
Comments will be reviewed, evaluated and given full consideration during decision-making process

## Slide 22: Project Resource Locations
INDOT Fort Wayne District Office
  5333 Hatfield Road, Fort Wayne, Indiana 46808
  Planning, Project Development/Delivery, Construction, Maintenance for Northeast Indiana
  http://www.in.gov/indot/2703.htm
Wabash Carnegie Public Library
188 West Hill Street, Wabash, IN 46992
Phone: (260) 563-2972
INDOT Office of Public Involvement
  100 North Senate Avenue, Room N642, Indianapolis, IN 46204
  Phone: (317) 232-6601
  rclark@indot.in.gov
Transportation Services Call Center
Provides citizen and business customers with a single point-of-contact to request transportation services, obtain information, or provide feedback through multiple channels of communications.
855-463-6848 • INDOT4U.com • INDOT@indot.in.gov

## Slide 23: Next Steps
Public and project stakeholder input
  Submit comments via options described on page 1 of information packet
INDOT review and evaluation
  All comments given full consideration during decision-making process
  Finalize/approve environmental document, complete project design
Communicate a decision
  INDOT will notify project stakeholders of decision
  Work through local media, social media outlets, paid legal notice
  Make project documents accessible via repositories
Questions? Contact Public Involvement Team
Project resource information on-line https://www.in.gov/indot/3896.htm

## Slide 24: Thank You
Please visit with the INDOT project team following the presentation and comment session
Project Open House
  Project maps, displays, INDOT project team and informal Q & A
  INDOT Fort Wayne District page: http://www.in.gov/indot/2703.htm